## Slide 1: Hazards of Excavations
This material was produced under a grant (SH-31234-SH7) from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does the mention of trade names, commercial products, or organization imply endorsement by the U.S. Government.

## Slide 2: Objectives
Identify what a trench is
Review fatality reports
Define definitions of different components of trenches
Identify hazards of the excavations
Identify protective measures

## Slide 3: What is a Trench?
Trench (Trench excavation) means a narrow excavation (in relation to its length) made below the surface of the ground. In general, the depth is greater than the width, but the width of a trench (measured at the bottom) is not greater than 15 feet (4.6 meters).
An excavation is any man-made cut, cavity, trench, or depression in an earth surface formed by earth removal.

## Slide 4: Fatality reports
U.S. Bureau of Labor Statistics (BLS) data show that 271 workers died in trenching or excavation cave-ins from 2000 through 2006.

## Slide 5: The greatest risk
Cave-ins are the leading cause of deaths with excavations
  Little to no warning before sidewall gives away
  One of the most hazardous construction operations
  Cubic yard of soil weights up to 3000 lbs.

## Slide 6: Osha Trench Compliance
https://www.youtube.com/watch?v=0wmcD3aM8X4
OSHA inspector enters a jobsite with individuals inside an excavation with inadaquate protection from the excavation hazards.
Notes: Source: https://www.youtube.com/watch?v=0wmcD3aM8X4
OSHA inspector enters a jobsite with individuals inside an excavation with inadaquate protection from the excavation hazards.

## Slide 7: Video Break down
What were the hazards of the excavation?
Was there any protection?
What could have been done differently?
Notes: Question 1
Hazards include; improper protection, falling dirt, utility lines, heavy equipment, ect.
Question 2
There was protection but not nearly tall enough to prevent dirt from falling in
Question 3
Having a competent person evaluate the excavation and protective system to ensure it is correct for that site.

## Slide 8: Introduction to Excavations
Source: https://www.youtube.com/watch?v=EIthR6akGtw
Video: This video shows definitions relating to excavations
Notes: Source: https://www.youtube.com/watch?v=EIthR6akGtw
Video: This video shows definitions relating to excavations

## Slide 9: Definitions
Excavation – a man-made cut, cavity, trench, or depression formed by earth removal.
Trench – a narrow excavation. The depth is greater than the width, but not wider than 15 feet.
Shield - a structure able to withstand a cave-in and protect employees
Shoring - a structure that supports the sides of an excavation and protects against cave-ins
Sloping - a technique that employs a specific angle of incline on the sides of the excavation. The angle varies based on assessment of impacting site factors.
Notes: Definitions taken from 29 CFR 1926

## Slide 10: When do you need protection?
All trenches 5 feet or deeper require a protective system unless the excavation is made entirely of stable rock.
Unprotected Trench
Notes: https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf
Picture Source: https://www.osha.gov/SLTC/etools/construction/trenching/mainpage.html

## Slide 11: General hazards
The greatest risk from excavations is cave-ins
Other risks while working inside or near an Excavation include:
  Water
  Inhalation hazards
  Lack of oxygen
  Underground utilities
  Equipment
  Spoils close to the edge
  Falls
  Egress

## Slide 12: Role of Competent person
OSHA standards require that employers inspect trenches daily and as conditions change by a competent person before worker entry to ensure elimination of excavation hazards
Competent Person- is one who is capable of identifying existing and predictable hazards in the surroundings or working conditions which are unsanitary, hazardous, or dangerous to employees, and who has authorization to take prompt corrective measures to eliminate them
Notes: https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf

## Slide 13: Excavations in Construction/Trenching
Source: https://www.youtube.com/watch?v=cFYkeT0Yk6k
Video: This video shows the importance of using a system to protect workers from excavation hazards, and having a competent person on site to ensure all hazards are eliminated.
Notes: Source: https://www.youtube.com/watch?v=cFYkeT0Yk6k
Video: This video shows the importance of using a system to protect workers from excavation hazards, and having a competent person on site to ensure all hazards are eliminated.

## Slide 14: Video Break down
What were the hazards of the excavation?
Was there any protection?
What could have been done differently?
Notes: Question 1
Hazards of this excavation was having no protective system for the workers in the excavation.
Question 2
There were no protective devices in place, the use of a protective device could have saved lives
Question 3
Having a competent person to evaluate the excavation and implementing a protective system for the workers inside the excavation.

## Slide 15: Cave-in protection
Four main types
  Shield - can be permanent or portable. Also known as trench box or trench shield.
  Shoring - such as metal hydraulic, mechanical or timber shoring system that supports the sides
  Sloping - form sides of an excavation that are inclined away from the excavation
  Benching - excavating the sides of an excavation to form one or a series of horizontal levels or steps
Notes: https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf

## Slide 16: Sloping
Inclining the trenching material away from the excavation, so in case of an cave in the material won’t fall from the sides crushing workers inside the excavation. Factors to take into account:
  Soil type
  Materials adjacent to excavation
  Work done around excavations
  Water
  Weather
Notes: https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf

## Slide 17: Shields
Shields are engineered structures that take into account the trenches many hazards, and minimizes the hazards of material falling into the excavation and injuring the occupants inside. Some of the factors to consider with shields are:
  Depth of cut
  Weather
  Water
  Material to be used in trench
  Other operations in the vicinity
  Spoil piles
Notes: https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf

## Slide 18: Shoring
Installing engineered supports directly to the walls of the excavation, it is designed to prevent soil movement. Factors to consider when using this protective system:
  Soil type
  Strengths of support system
  Water
  Weather
  Work done around excavation
Notes: https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf

## Slide 19: Benching
Benching is the act of cutting shelves into the sidewalls of the excavation to ensure if there is a cave-in the trench material will not cause harm to the worker. Things to take into consideration with this protective system:
  Soil type
  Weather
  Water
  Other operations onsite
Notes: https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf

## Slide 20: Other Hazards inside an Excavation include:
  Water
  Inhalation hazards
  Lack of oxygen
  Underground utilities
  Equipment
  Spoils close to the edge
  Falls
  Egress
  Ergonomic
  Temperature extremes

## Slide 21: Water
Causes the sides to become unstable
Cave-ins
Drowning hazard
Electrocution hazard if electrical equipment present
Inspect trenches following a rainstorm or other water intrusion

## Slide 22: Inhalation hazards
Carbon Monoxide
  Bonds with the cells hemoglobin
    50 times tighter
    200 times stronger
  Compared to oxygen's bond to hemoglobin
Work done in the excavation
  Painting
  Welding

## Slide 23: Lack of Oxygen
Room Oxygen -21%
  Oxygen Deficient ≤ 19.5%
  Oxygen Enriched ≥ 23.5%
Oxygen can be displaced
  Different gasses and compounds in the trench and surrounding area
  The work performed in the trench
Oxygen can be absorbed
  Rust is the oxidization of metal
  Chemical processes in the trench

## Slide 24: Underground utilities
Water
  We already discussed
Electrical
  Electrocution hazard- 75 mA can cause cardiac arrest
Natural Gas
  Explosion hazards- high pressures are used to transport natural gas through underground lines
Always locate lines before you begin excavations, ensure all lines uncovered are supported properly

## Slide 25: Equipment
Can cause inhalation hazards
  Carbon Monoxide
Tip into trench
  If the trench is unseen use barriers to prevent equipment from getting to close
Cause a cave-in
  Moving earth equipment
  Vibrations from equipment

## Slide 26: Spoil Pile (excavated soil)
Spoil piles need to be located at least 2 feet away from the edge of the excavation, and it may need to be further away depending on conditions.
  Causes extra weight on the trench walls
  Even properly supported trench can be dangerous if spoil can fall into excavation

## Slide 27: Falls
To ensure the excavation is safe from falls
  Place a barrier around the excavation to ensure everyone knows where it is
  Place bright colored or reflective tape around to see in low light conditions
  Ensure signs are properly posted to ensure the excavation location is apparent
  Fall protection required at 6’

## Slide 28: Egress
OSHA standards require safe access and egress to all excavations, including ladders, steps, ramps, or other safe means of exit for employees working in trench excavations 4 feet or deeper
  Located within 25’ of all workers

## Slide 29: Ergonomic
Study of how environmental factors effect the body
  Body mechanics
  Using equipment
  Right tool for the job
  Job rotation
  Repetitive motion injuries

## Slide 30: Temperature extremes
Cold Stress
Cold stress occurs by driving down the skin temperature and eventually the internal body temperature (core temperature).
This may lead to serious health problems, and may cause tissue damage, and possibly death.
Heat Stress
from heat rash and heat cramps to heat exhaustion and heat stroke. Heat stroke can result in death.
requires immediate medical attention.
Notes: https://www.osha.gov/SLTC/heatstress/
https://www.osha.gov/SLTC/emergencypreparedness/guides/cold.html

## Slide 31: Hazard Identification

## Slide 32: Hazard identification
Shoring not adequate
No real protective system
Limited access zone
Vehicles in close proximity
Notes: Source: https://www.osha.gov/SLTC/etools/construction/trenching/mainpage.html

## Slide 33: Hazard Identification
Improper benching
No egress
Unprotected edge
Notes: https://www.osha.gov/SLTC/etools/construction/trenching/mainpage.html

## Slide 34: Hazard Identification
These workers are not protected from a cave-in, nor do they have any apparent safe access or egress from the trench
Notes: https://www.osha.gov/SLTC/etools/construction/trenching/mainpage.html

## Slide 35: Worker Rights and responsibilities

## Slide 36: Employee Rights & Responsibilities Occupational Safety and Health Act of 1970
To assure safe and healthful working conditions for working men and women
By authorizing enforcement of the standards developed under the Act
By assisting and encouraging the States in their efforts to assure safe and healthful working conditions
By providing for research, information, education, and training in the field of occupational safety and health…
Notes: Workers Rights
http://www.osha.gov/Publications/osha3021.pdf
The instructor will discuss employee rights and responsibilities with the participants.

## Slide 37: Employee Rights & Responsibilities
You have the right to:
  A safe and healthful workplace
  Know about hazardous chemicals
  Information about injuries and illnesses in your workplace
  Complain or request hazard correction from employer
Notes: The information above was taken from the new 2 hour Intro to OSHA PPT, slide #10.
The instructor will discuss employee rights and responsibilities with the participants.

## Slide 38: Employee Rights & Responsibilities You have the right to:
File a confidential complaint with OSHA to have their workplace inspected.
Receive information and training about hazards, methods to prevent harm, and the OSHA standards that apply to their workplace. The training must be done in a language and vocabulary workers can understand.
Get copies of their workplace medical records and exposure records.
Participate in an OSHA inspection and speak in private with the inspector.
Notes: Workers Rights
http://www.osha.gov/Publications/osha3021.pdf

## Slide 39: Employee Rights & Responsibilities Continued:
File a complaint with OSHA if they have been retaliated or discriminated against by their employer as the result of requesting an inspection or using any of their other rights under the OSH Act.
File a complaint if punished or discriminated against for acting as a “whistleblower” under the additional 21 federal statutes for which OSHA has jurisdiction.
Notes: Workers Rights
http://www.osha.gov/Publications/osha3021.pdf
Incorporate into all 4 modules. 3-4 slides need to be added. Provide handouts to minimize amount of info on slides.

## Slide 40: Whistleblower Protection
http://www.whistleblowers.gov/
Notes: The Whistleblower Protection Program
http://www.whistleblowers.gov/