## Slide 1: Chemical Safety

## Slide 2: Chemical Hazards
Flammable
Corrosive
Reactive
Toxic

## Slide 3: Chemical Hazards
Reference Scales
How flammable?
How Corrosive?
How Reactive?
How Toxic?
Detection equipment
M8/M9 Tape
Combustible Gas Indicator
Monitoring for Chemical Agents
Meter
ADP 2000
CAM
HAPSITE
portable GG/MS
PIDs

## Slide 4: Flammable
Fire triangle (tetrahedron)
fuel O2
ignition source
chemical chain reaction

## Slide 5: Flammable
Flash pt: minimum temp for combustion (lab) OSHA 100F EPA Haz waste 140F
DOT 100F
Examples:
ether = -40F gasoline -45F
styrene =88F
stoddard solvent 110F cresol=187F

## Slide 6: Flammable
Flammable range: range in air that can
support combustion; percent % of flammable in air/ amt of vapor needed to support combustion at a liquid's surface depends on volatility of liquid/vapor pressure
LEL/LFL UEL/UFL
Gasoline 1.4---------------7.6 %
Formaldehyde 7--------73%
Ammonia 15----------28%

## Slide 7: Flammable
Labels and Markings
Flash point and Flammable range : SDS, NIOSH pocket Guide
Instrument to detect flammable
ranges. {CGI}

## Slide 8: Corrosive
Any compound that can cause rapid damage to human tissues, metals, solids
pH-Hydrogen ion concentration scale 1[strong acids] to
14[strong bases Alkali]

## Slide 9: Corrosive
Secondary Problems:
Liberation of flammable toxic vapors
Generate heat
Combustion of other materials O2

## Slide 10: Corrosive
Labels and Markings
pH paper
Where on pH scale 7=neutral

## Slide 11: Reactive
Chemical naturally or designed to bring about a chemical reaction
(Molecules align into long chains)
React with other chemicals

## Slide 12: React with
air/light: hydrogen and chlorine reacts with light
Water: sodium, magnesium, strong acids
Self reactive: inherently unstable (heat/ light/ shock/ age)
(Styrene, ethylene as they age decompose creating heat: the hotter they get the more they accelerate a reaction.)

## Slide 13: Reactive
No detection instruments or reference scales
Rely on sources: Chemical Dictionary SDS
NIOSH Guide Labels

## Slide 14: Toxic
Exposure limits
Detection instruments
Reference Sources
Image of a sotra

## Slide 15: How Chemicals Behave
Vapor Pressure [tendency to evaporate into air]
Vapor Density [heavier of lighter than air]
Specific Gravity [ sink or float in water]
Provides clues to exposure and methods of control
SDS NIOSH Guide

## Slide 16: June 1, 2015 requirements
By June 1, 2015, all labels will be required to have pictograms, a signal word, hazard and precautionary statements, the product identifier, and supplier identification.
Hazard Pictograms
Signal Word
'Danger'
Hazard Statement
'Highly flammable liquid and vapor.
May cause liver and kidney damage.'

## Slide 17: Thank you for your attention.
This material was produced under grant number SH-26285-SH4 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.