## Slide 1: Machine Guarding

## Slide 2: Disclaimer
This material was produced under grant number
SH-05029-SH8 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government..

## Slide 3: OSHA’s Mission
With the Occupational Safety and Health Act of 1970, Congress created the Occupational Safety and Health Administration (OSHA) to assure safe and healthful working conditions for working men and women by setting and enforcing standards, providing training, outreach, education and assistance. Additional information can be found on the OSHA Website at https://www.osha.gov/

## Slide 4: OSHA’s Whistleblower Protection Program
This program enforces the whistleblower provisions of more than 20 whistleblower statutes protecting employees who report various workplace violations. In general, the whistleblower anti-retaliation provision provide that employers may not discharge or otherwise retaliate against an employee because the employee has filed a complaint or exercised any rights provided to employees. More information can be found on the Whistleblowers Website at https://www.whistleblowers.gov/

## Slide 5: Agenda
Accidents Related to Unguarded Equipment
Elements of a Machine Guarding Program
OSHA Regulations for Machine Guarding
Types of Guards and Devices
Guarding by Location and Distance
Robots in the Workplace
Hazards of Unguarded Machines
Requirements for Guarding
Workshop discussion for practical application of various type of guards and devices

## Slide 6: OSHA Data – Accident Search Results (Keyword: machine guarding)
Event Date: 01/26/2018 – Employee is killed by tire recycling shredder
Event Date: 01/25/2018 – Employee dies after being caught in auger
Event Date: 11/17/2017 – Employee amputates three fingertips clearing jammed vacuum sealer
Event Date: 11/16/2017 – Employee catches gloved hand on a rotating shaft and suffered a compound fracture to his left wrist

## Slide 7: OSHA Data – Accident Search Results (Keyword: machine guarding) (continued)
Event Date: 11/07/2017 – Employee fractures skull while operating a CNC machine
Event Date: 11/06/2017 – Employee’s right ring finger is amputated by hydraulic press
Event Date: 11/03/2017 – Employee is troubleshooting equipment and amputated the tip of middle finger and broke his ring finger
Event Date: Employee catches finger between chain and sprocket and amputates his right hand index finger

## Slide 8: Statistics
Workers who operate and maintain machinery suffer approximately 18,000 amputations, lacerations, crushing injuries, abrasions, and over 800 deaths per year in the United States
(Sources: OSHA website)

## Slide 9: Statistics – National Safety Council-Injury Facts - 2016
The top three leading causes of work-related injuries:
  #1 Overexertion, bodily reaction
  #2 Contact with objects/equipment
  #3 Falls, slips, trips

## Slide 10: Statistics – National Safety Council-Injury Facts – 2016 (continued)
Contact with objects/equipment
  Injury rate: 23.9 per 10,000 full-time workers
  Age group most at risk 16 to 24
  Industry most at risk: agriculture, construction and extraction, and transportation and warehousing
  Typical days lost: 5
  Most frequent type of injury: cuts, lacerations, punctures

## Slide 11: Common Machine-related Injuries
Death
Crushing wounds
Cutting and tearing
Puncture wounds
Shearing wounds
Spraining and straining
PTSD*

## Slide 12: PTSD – Workers don’t return from injury
Did you know that many workers who sustain both minor and major injuries, including compensable injuries, within weeks or months suffer from episodes of depression?
A study, “Incidence of Depression After Occupational Injury,” conducted by the U.S. Centers for Disease Control and Prevention (CDC) and drawing on nearly 367,900 injured and non-injured workers from a 2005 database, found that the odds of injured workers being treated for depression were 45% higher than those of non-injured workers.

## Slide 13: Machines are essential
How do we prevent injuries, amputations, and even death when working with machinery?

## Slide 14: Machine Guarding Safety Program
Compliance with:
  29 CFR 1910 Subpart O (General Industry)
  29 CFR 1926 Subpart I (Construction Industry)
  29 CFR 1928 Subpart D (Agriculture Industry)
Lockout/Tagout
Safe Work Practices
Warnings
Inspections
Enforcement
Training

## Slide 15: 1910.212 – General requirements for all machines (horizontal standard)
1910.212(a)(1) Types of guarding. One or more methods of machine guarding shall be provided to protect the operator and other employees in the machine area from hazards such as those created by point of operation, ingoing nip points, rotating parts, flying chips and sparks. Examples of guarding methods are-barrier guards, two-hand tripping devices, electronic safety devices, etc.
19210.212(a)(2) General requirements for machine guards. Guards shall be affixed to the machine where possible and secured elsewhere if for any reason attachment to the machine is not possible. The guard shall be such that it does not offer an accident hazard in itself
Notes: There are two type of standards: Horizontal and Vertical Standard. Horizontal standards are standards that apply across the many different types of industries. Vertical standards are standards that apply to specific industries, such as: wood working, hydraulic presses, etc.. In General Industry 1910, standard 1910.212(a)(1) and 1910.212(a)(2) are board in nature and encompasses all industries that fall under the 1910 standard. In summary if any part of your body can come into contact with a moving part and/or you can be exposed to flying debris, there must be a guard to protect the workers.

## Slide 16: Check Your Knowledge
Machinery, such as grinders or buffers when secured to a work bench, the work bench must be securely anchored to prevent walking or moving?
(reference standard interpretations/Interlock requirements for access door(s) of trash compactor)

## Slide 17: 1926.300 General requirements
1926.300(b)(1) When power operated tools are designed to accommodate guards, they shall be equipped with such guards when in use.
1926.300(b)(2) Belts, gears, shafts, pulleys, sprockets, spindles, drums, fly wheels, chains, or other reciprocating, rotating or moving parts of equipment shall be guarded if such parts are exposed to contact by employees or otherwise create a hazard. Guarding shall meet the requirements as set forth in American National Standards Institute, B15.1-1953 (R1958), Safety Code for Mechanical Power-Transmission Apparatus.

## Slide 18: 1928.57 – Guarding of farm field equipment, farmstead equipment, and cotton gins.
1928.57(a)(1) Purpose. The purpose of this section is to provide for the protection from the hazards associated with moving machinery parts of farm field equipment, farmstead equipment, and cotton gins used in any agricultural operations.
1928.57(a)(6)(i) Keep all guards in place when the machine is in operation;
1928.57(a)(7) Methods of guarding….
1928.57(a)(8) Strength and design of guards

## Slide 19: 1928.57 – Guarding of farm field equipment, farmstead equipment, and cotton gins. (continued)
1928.57(b) Farm field equipment
1928.57(b)(2) Other power transmission components
1928.57(c) Farmstead equipment
1928.57(d) Cotton gin equipment

## Slide 20: Check Your Knowledge
Per the OSHA Agriculture regulations, employees operating or servicing all covered equipment all required to receive operating instructions at the time of initial assignment?
(reference 1928.57(a)(6))

## Slide 21: Check Your Knowledge
Per the OSHA Agriculture regulations, unless otherwise specified, each guard and its support shall be capable of withstanding the force that a (XXX) pound individual, leaning against the guard, would exert upon the guard?
(reference 1928.57(a)(8)(ii))

## Slide 22: Check Your Knowledge
All tractors shall be equipped with an agricultural tractor master shield on the rear power take-off with no exceptions?
(reference 1928.57(b)(1)(i))

## Slide 23: Types of Guards
Fixed
Interlocked
Adjustable
Self-adjusting

## Slide 24: Fixed
What is the purpose?
  Provides a barrier
Advantages
  Suitable for many applications
  In-house fabrication
  Provides maximum protection
  Usually requires minimum maintenance
  Suitable for high production, repetitive operations

## Slide 25: Fixed (continued 1)
What is the purpose?
  Provides a barrier
Limitations
  Interferes with visibility
  Limited to specific operations
  Machine adjustments and repair often requires its removal

## Slide 26: Fixed (continued 2)
What is the purpose?
  Provides a barrier

## Slide 27: Examples of fixed guards

## Slide 28: Interlocked
What is the purpose?
  Shuts off or disengages power and prevents starting of machine when guard is open
Advantages
  Can provide maximum protection
  Allows access to machine for making minor adjustments or removing jams without removal of fixed guards

## Slide 29: Interlocked (continued 1)
What is the purpose?
  Shuts off or disengages power and prevents starting of machine when guard is open
Limitations
  Requires careful adjustment and maintenance

## Slide 30: Interlocked (continued 2)
What is the purpose?
  Shuts off or disengages power and prevents starting of machine when guard is open

## Slide 31: Check Your Knowledge
Is an interlock required on the side door of a trash compactor, if the side door is located 55 inches from ground level, and the door is closed and lathed while the compactor is cycling
(reference standard interpretations/Guarding machines on moveable benches and pedestals)

## Slide 32: Adjustable
What is the purpose?
  Provides a barrier that may be adjusted to facilitate a variety of production operations
Advantages
  Can construct to suit many specific operations
  Adjustable to allow for varying sizes of material

## Slide 33: Adjustable (continued 1)
What is the purpose?
  Provides a barrier that may be adjusted to facilitate a variety of production operations
Limitations
  Hands may enter danger area
  May require frequent maintenance and adjustment
  The guard may be tampered with by the operator

## Slide 34: Adjustable (continued 2)
What is the purpose?
  Provides a barrier that may be adjusted to facilitate a variety of production operations

## Slide 35: Check Your Knowledge
Cutting saw blade or abrasive wheels: Is D’AX wheels considered to be cutting or abrasive wheels in regards to OSHA guarding requirements?
(reference standard interpretations/D’AX wheels are to be guarded as cutting saws)

## Slide 36: Self-adjusting
What is the purpose?
  Provides barrier that moves according to size of material entering the danger zone
Advantages
  Off-the-shelf guards often commercially available

## Slide 37: Self-adjusting (continued 1)
What is the purpose?
  Provides barrier that moves according to size of material entering the danger zone
Limitations
  Does not always provide maximum protection
  May interfere with visibility
  May require frequent maintenance and adjustment

## Slide 38: Self-adjusting (continued 2)
What is the purpose?
  Provides barrier that moves according to size of material entering the danger zone

## Slide 39: Types of Devices
Presence sensing devices
Restraints
Pullback devices
Safety trip controls
Gates

## Slide 40: Presence Sensing Devices (continued 1)
What is the purpose?
  Disengage the machine when something is detected in the hazard zone
Types
  Photoelectric
  Radiofrequency
  Electromagnetic

## Slide 41: Presence Sensing Devices (continued 2)
What is the purpose?
  Disengage the machine when something is detected in the hazard zone
Advantages
  All three types can allow free movement for operator
  Simplicity of use
  Photo electrics requires no adjustment
Limitations
  Failures of input/output devices resulting in no detection when something is in the danger zone

## Slide 42: Presence Sensing Devices (continued 3)
What is the purpose?
  Disengage the machine when something is detected in the hazard zone
Limitations
  Does not protect against mechanical failure
  Limited to equipment that can be stopped
  Sensitivity of antennae may be an issue
  Contact bar or probe must be properly adjusted for each application(electro-mechanical)

## Slide 43: Check Your Knowledge
Does OSHA have any prohibition on the use of Presense Sensing Device Initiation (PSDI) light curtains in regard to: Mechanical Power Presses, and Hydraulic Welding Presses?
(reference standard interpretations/The use of Presense Sensing Device Initiation light curtains in regard to Mechanical Power Presses, Hydraulic Power Presses and Hydraulic Welding Presses)

## Slide 44: Restraint
What is the purpose?
  Prevents the operator from reaching into the danger area
Advantages
  Little risk of mechanical failure

## Slide 45: Restraint (continued)
What is the purpose?
  Prevents the operator from reaching into the danger area
Limitations
  Limits movements of operator
  Requires close supervision of operator’s use of equipment
  Requires frequent inspection, maintenance and adjustments

## Slide 46: Check Your Knowledge
Does OSHA have a regulation for machine guarding specific to the bowling pin setting machinery?
(reference standard interpretations/OSHA ARCHIVE regarding the subject of guarding machinery in bowling centers)

## Slide 47: Pullback
What is the purpose?
  As the machine cycle, the operator’s hands are pulled out of the danger zone
Advantages
  Eliminates the needs for guards at the danger zone

## Slide 48: Pullback (continued)
What is the purpose?
  As the machine cycle, the operator’s hands are pulled out of the danger zone
Limitations
  Limits movements of operator

## Slide 49: Safety trip controls
What is the purpose?
  Stops machine when controls tripped
Types
  Pressure sensitive body bar
  Safety triprod
  Two-hand control
  Two-hand trip

## Slide 50: Safety trip controls (continued 1)
What is the purpose?
  Stops machine when controls tripped
Advantages
  Simplicity in use
  Concurrent use of both hands on separated controls prevent hands from being in danger zone

## Slide 51: Check Your Knowledge
Does machine safeguarding requirements apply to refuse balers, compactors and garbage trucks?
(reference standard interpretations/Machine safeguarding requirements apply to refuse industry balers, compactors, and garbage trucks)

## Slide 52: Safety trip controls (continued 2)
What is the purpose?
  Stops machine when controls tripped
Limitations
  Only protects the operator
  May require a machine brake
  Operator may block one control open

## Slide 53: Gates
What is the purpose?
  Provided a barrier between danger area and operator or other personnel
Advantages
  Can prevent reaching into or walking into the danger zone

## Slide 54: Gates (continued)
What is the purpose?
  Provided a barrier between danger area and operator or other personnel
Limitations
  May require frequent inspection and regular maintenance
  May interfere with the operator’s ability to see the work

## Slide 55: Guarding by Location and Distance
Location
  Position machines so that the dangerous moving parts of a machine are not accessible, or do not present a hazard to the worker during the normal operation of the machine
    Minimum distance required from floor to danger zone is 7 feet.
Distance
  D = 63 in/s x Ts
      D is inches from the point of operation
      63 in/s is an assumed hand speed
      Ts is the stopping time of the machine in seconds

## Slide 56: Check Your Knowledge
Are barrier chains or fencing surrounding the working envelope and employer training and work procedures which prohibit employee access into the work area be considered adequate machine guarding?
(reference standard interpretations/machine guarding and exposure to hazards from robotic laundry shuttles)

## Slide 57: Types of Machine Motion
1 Rotating
  List examples of rotating motion at your place of employment
  Identify hazards resulting for rotating motion
    Point of operation, In-running nib points, chips, sparks
  Are the examples listed; guarded or unguarded?
    If not Why?
  Share examples of how rotating motion are guarded at your place of employment
  Discussion of Requirements for machine guards

## Slide 58: Discussion on Requirements for Machine Guarding (rotating)
Does the current guarding method prevent contact?
  Does the guard openings width meet the requirement for the distance a guard must be from a danger line?
Is the machine guard secure?
Does the machine guard create no new Hazards?

## Slide 59: Discussion on Requirements for Machine Guarding (rotating continued 1)
Does the guard protect from falling objects?
Does the guard create no interference?
Does the guard allow for safe lubrication?
Does the guarding method allow for work to be done?

## Slide 60: Table O-10
In the 2010 release of ANSI 11.19 there were two fundamental changes:
1: ANSI B11.19 (2010) now applies o ALL machines and equipment.
2: There is no longer any difference between the guarding standards for
- Point of Operation
- Mechanical Transmission Apparatus

## Slide 61: Types of Machine Motion (tranverse)
2 Transverse Motions
  List examples of transverse motion at your place of employment
  Identify hazards resulting for tranverse motion
  Are the examples listed; guarded or unguarded?
    If not Why?
  Share examples of how transverse motion are guarded at your place of employment
  Share concerns/issues with current guarding methods

## Slide 62: Discussion on Requirements for Machine Guarding (tranverse)
Does the current guarding method prevent contact?
  Does the guard openings width meet the requirement for the distance a guard must be from a danger line?
Is the machine guard secure?
Does the machine guard create no new Hazards?
Does the guard protect from falling objects?
Does the guard create no interference?
Does the guard allow for safe lubrication?

## Slide 63: Types of Machine Motion (cutting)
3 Cutting Action
  List examples of cutting action at your place of employment
  Identify hazards resulting for cutting action
  Are the examples listed; guarded or unguarded?
    If not Why?
  Share examples of how cutting actions are guarded at your place of employment
  Share concerns/issues with current guarding methods

## Slide 64: Discussion on Requirements for Machine Guarding (cutting)
Does the current guarding method prevent contact?
  Does the guard openings width meet the requirement for the distance a guard must be from a danger line?
Is the machine guard secure?
Does the machine guard create no new Hazards?
Does the guard protect from falling objects?
Does the guard create no interference?
Does the guard allow for safe lubrication?

## Slide 65: Types of Machine Motion (sheet metal)
4 Punching, Shearing, and Bending
  List examples of punching, shearing and bending at your place of employment
  Identify hazards resulting for punching, shearing and bending
  Are the examples listed; guarded or unguarded?
    If not Why?
  Share examples of how cutting actions are guarded at your place of employment
  Share concerns/issues with current guarding methods

## Slide 66: Discussion on Requirements for Machine Guarding (sheet metal)
Does the current guarding method prevent contact?
  Does the guard openings width meet the requirement for the distance a guard must be from a danger line?
Is the machine guard secure?
Does the machine guard create no new Hazards?
Does the guard protect from falling objects?
Does the guard create no interference?
Does the guard allow for safe lubrication?

## Slide 67: Robots in the Workplace
What are industrial robots?
  Programmable multifunctional mechanical devices
  Designed to move:
    Material
    Parts
    Tools
    Specialized devices
An industrial robot system
  Includes an industrial robot
  devices and/or sensors
  Sequencing or monitoring communication devices

## Slide 68: Robots in the Workplace (continue)
Why robots?
  Used to perform work that is unsafe, hazardous for humans
  Highly repetitive and unpleasant tasks
Features of robots
  Small to large lifting capacity
  High speed
  High torque
  Six-axis articulation
  High payload positioning accuracy

## Slide 69: Types and Classification of Robots
Source: OSHA web site

## Slide 70: Accidents related to Robots
Studies in Sweden and Japan indicates that many robot accidents do not occur under normal operating conditions but, instead during:
  Programming
  Program refinement
  Maintenance and repair
  Testing
  Setup and adjustment
All these operations may require personnel to be temporarily within the robot’s working envelope

## Slide 71: Typical accidents related to robots
A robot’s arm functioned erratically during programming sequence and struck operator
A materials handling robot operator entered a robot’s work envelope during operations and was pinned between the back end of the robot and safety pole
A fellow employee accidentally tripped the power switch while a maintenance worker was servicing an assembly door. The robot’s arm struck the maintenance worker’s hand

## Slide 72: Sources of hazards
Moving mechanical components causing:
  Trapping
  Crushing
  Death
Stored energy
  electrical,
  Hydraulic
  Pneumatic
  Gravity
    NOTE: unexpected release of stored energy can result in sudden drop of payload, axis arms, etc.

## Slide 73: Sources of hazards (continued1)
Hazardous atmospheres, explosive/combustible materials, high or low temperatures
  The use of industrial robots to eliminate safety concerns to employees, does not eliminate the safety concerns for those doing maintenance or programming of the robots
Inadvertent operation caused by equipment failure
Actions by personnel, either unintended or deliberate

## Slide 74: Eliminating the hazards
Barrier guards, fixed and interlocked
Safety light curtains/screens
Area scanning safeguarding devices
Radio frequency/capacitance safeguarding devices
Safety mat systems
Single and multiple beam safety systems
Two hand control systems

## Slide 75: Questions