## Slide 1: Crystalline Silica Awareness Training Water Utility Operators and Construction Laborers

## Slide 2: OSHA Susan Harwood Grant
This material was produced under Grant Program #SH-05058-SH8 from the OSHA, U.S. Department of Labor. It Does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mentioning of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revised from grant number SH-29666-SH6.

## Slide 3: Class Room Participation
The instructor encourages open dialog
Participants can ask questions anytime during the training presentation
Media materials will be presented to the class to discuss, assess and identify the possible hazards to excavation and trenching activities
Notes: We realize and appreciate that we have highly trained operators in each field of work and other competent workers in this classroom. Please feel free to add to any content, experience or lessons learned in addition to our training materials. We value your knowledge and input.

## Slide 4: Breaks!
There will be 10 minutes breaks as needed throughout the training period

## Slide 5: Questions and Feed Back
At the end of the presentation participants will be ask to fill out a brief questionnaire and provide feedback on the training materials

## Slide 6: Training Objectives
      What is silica?
      Silica history
      OSHA Standards on silica
      Silica exposure control methods for construction
      Mandatory requirements for silica exposure control
      Alternative exposure control methods
      Program and medical surveillance

## Slide 7: What is Silica?
Crystalline silica is a common mineral found in many naturally occurring and man-made materials used at construction sites - Examples:
  Sand
  Concrete
  Brick
  Block
  Stone
  Mortar
Image from remodeling magazine

## Slide 8: What is Respirable Crystalline Silica Continued?
Silica – very small jagged particles, like tiny shards of glass-that can be generated by high-energy operations like:
  Cutting
  Sawing
  Grinding
  Drilling
  Crushing and abrasive blasting (of silica containing materials)
Image of Crystalline Silica from the NIOSH doc

## Slide 9: Respirable Crystalline Silica History
Exposure to respirable crystalline silica is one of the oldest and best documented occupational health risks.
In 1700, Dr. Bernardo Ramazzini (the founder of occupational medicine) found evidence of silicosis in stone cutters.
In Early 1900’s Dr. Alice Hamilton documented silica related illnesses among granite workers.
By the 1930’s these granite workers successfully bargained for the installation of ventilation equipment in their work sheds.

## Slide 10: Respirable Crystalline Silica History Continued
Despite Drs. Ramazinni and Hamilton’s work, RCS exposures and silicosis deaths continued.
Most significantly was the Hawk’s Nest Tunnel disaster in the 1930’s.
Estimated 764 out of 1,213 men who worked underground for at least two months contracted silicosis and died within five years of project completion.

## Slide 11: Silica Standards
  OSHA has issued a new standard (CFR 1926.1153) to curb silica related diseases in the US workers by limiting their exposure to silica
    Increasing workers’ awareness of the serious health hazards of silica dust
    Providing the knowledge necessary to perform work safely when there is silica exposure, and ways to limit silica exposure to levels below the Permissible Exposure Limit (PEL)

## Slide 12: Regulatory Agencies
Prevention and elimination of silicosis and silica-related disease in United States are priorities of
  National Institute for Occupational Safety and Health (NIOSH)
  Occupational Safety and Health Administration (OSHA)
  Mine Safety and Health Administration (MSHA)
  American Lung Association

## Slide 13: Silica Related OSHA Standards
Several OSHA standards and directives cover operations that may expose workers to silica
  Air Contaminants (29 CFR 1910.1000)
  Hazard Communication (29 CFR 1910.1200)
  Respiratory Protection (29 CFR 1910.134)
  Ventilation (29 CFR 1926.57)
  Respirable Crystalline Silica (29 CFR 1926.1153)
OSHA’s Directive CPL 03-00-007 - National Emphasis Program- Crystalline
  Silica hazards
  Guidelines for air sampling
  Guidance on calculating PELs for dust containing silica
  Other compliance information (OSHA’s Directive CPL 03-00-007)

## Slide 14: OSHA’s Silica Standard Definitions
Employee Exposure: Exposure to airborne silica if employees were not using a respirator.
Permissible Exposure Limit (PEL) is the maximum amount or concentration of a chemical that a worker may be exposed to under OSHA regulations.
A time-weighted average is used to calculate a workers daily exposure to a hazardous substance (such as chemicals, dusts, fumes, mists, gases, or vapors) in an 8 hour work day
Action levels are used by OSHA and NIOSH to express a health or physical hazard. They indicate the level of a harmful or toxic substance/activity which requires medical surveillance, increased industrial hygiene monitoring

## Slide 15: OSHA Standard Permissible Exposure Limit and Action Level
Permissible Exposure Limit (PEL)
8-hour time-weighted average exposure limit (TWA)
Action level
(AL)
25 μg/m3 TWA
in the air
50μg/m3 TWA
in the air
If dust containing silica is visible in the air, there is a higher likelihood/chance that permissible exposure limit (PEL) is exceeded !
Construction
Construction

## Slide 16: Classroom Activity-OSHA PEL

## Slide 17: How Much Silica Dust is Too Much?
The safest amount of silica in the air is zero.
It only takes a very small amount of very fine respirable silica dust to create a health hazard.
Rule-of-thumb:
If dust containing silica is visible in the air, there is a higher chance of overexposure

## Slide 18: Health Risk Associated with Silica Exposure
  Silicosis – irreversible, low to moderate exposure, often disabling, and sometimes fatal lung disease. One may develop TB.
  Lung cancer-occurs after exposures to very high concentrations of silica
  Chronic obstructive pulmonary disease (e.g., bronchitis)
  Kidney and immune system diseases

## Slide 19: Types of Silicosis
    Acute form:
  Intense exposure to respirable dust of high crystalline silica content for a relatively short period (few months to less than 2 years)
    Accelerated form:
  Resulting from about 5-15 years of heavy exposure to respirable dusts of high crystalline silica content
    Chronic form:
  Most common form
  Less intense exposure and usually more than 20 years
Image of Crystalline Silica in lungs

## Slide 20: Silicosis an Occupational Lung Disease
Signs and Symptoms
Shortness of breath
Fever
Bluish skin at the ear lobes or lips
Disease progression
Fatigue
Extreme shortness of breath
Loss of appetite
Chest pain
Respiratory failure

## Slide 21: Classroom Activity-Silica Tables

## Slide 22: MATERIALS Are any of these involved?
Abrasive blasting
pavement manufacturing
Blast furnaces
Cement manufacturing
Ceramics, clay, and pottery
Concrete mixing
Concrete Asphalt tunneling
Construction (mainly cement, concrete work)
Demolition
Electronics industry
Foundry industry: grinding, molding, shakeout, core room (High Risk)
Hand molding, casting, and forming
Jack hammer operations
Manufacturing abrasives, paints, soaps, and glass
Mining
Repair or replacement of linings of rotary kilns and cupola furnaces
Rolling and finishing mills
Sandblasting (High Risk)
Setting, laying, and repairing railroad track
Steelwork
Stone, brick, and concrete block cutting, blasting, chipping, grinding, and sawing
Tunneling operations
INDUSTRY Do you work in any of these?
Abrasives
Coal Dust
Concrete
Filter Aids
Graphite, natural
Mica
Mineral Products
Paints
Pavement
Perlite
Plant Materials
Plastic Fillers
Polishing Compounds
Portland Cement
Sands
Silicates
Slag
Soapstone
Soil
Brickmason / stonemason
Blasting/drilling
Construction laborer
Crane and tower operator
Crushing and grinding machine operator
Drywall installation
Furnace, kiln, non-food oven operator
Heavy Equipment operator
Grinding, abrading, buffing, and polishing machine operator
Hand molder/shaper (not jeweler)
Heavy-equipment mechanic
Janitor or cleaner
Machinist
Metals/plastics machine operator
Molding and casting machine operator
Mining machine operator
Miscellaneous material moving equipment operator
Millwright
Operating engineer
Painter who sandblasts (High Risk)
Production supervisor
Rock driller (High Risk)
Roof bolter (High Risk)
Sandblaster (High Risk)
Steelworker
Welder/cutter
OCCUPATIONS Are you one of these?

## Slide 23: Silica Exposure Control Methods for Construction
The first step for an employer is to determine if the standard applies to the worker
If the work is covered by the standard, the new standard provides flexible alternatives. Employers can either choose;
Specified exposure control methods-Use a control method laid out in Table 1 of the construction standard; or
Alternative exposure control methods-Measure workers’ exposure to silica and independently decide which dust control methods work best to limit exposures to the PEL in their workplaces

## Slide 24: Silica Control Methods for Construction
Table 1
  Lists 18 common tasks covering equipment found on construction sites
  Describes engineering controls or control methods when working with materials containing silica
  Employers who comply with Table 1 are not required to conduct exposure assessments, or comply with the PEL threshold for workers engaged in tasks creating exposures.

## Slide 25: Engineering Controls
If silica is generated, OSHA requires engineering controls involving a mechanical process to eliminate exposure to silica dust
2 main methods are used to control silica dust while operating
Integrated water delivery system (IWDS)
Vacuum dust collection system (VDCS)

## Slide 26: Integrated Water Delivery Controls
  Water is supplied to equipment by
    a pressurized container,
    a constant water source e.g. a hose connected to a faucet
  Using water will usually reduce levels to below the PEL in construction activities

## Slide 27: Integrated Water Delivery Controls Continued
  An adequate supply of water for dust suppression is needed (at the flow rates specified by the manufacturer)
  The spray nozzle must be working properly to apply water at the point of dust generation
  The spray nozzle should not be clogged or damaged
  All hoses and connections must be intact.

## Slide 28: Integrated Water Delivery System Secondary Exposures Controls
  Limit secondary exposure by cleaning up any slurry generated
  In cold temperatures, where there is a risk of water freezing
  Electrical hazards

## Slide 29: Vacuum Dust Collection Equipment
  Good method for reducing silica exposures, but may not reliably keep exposure below PEL
  Include dust collector (hood or shroud), vacuum, hose and filters.

## Slide 30: Vacuum Dust Collection Controls
Include a dust collector (hood or shroud), vacuum, hose and filter(s)
  Adequate suction to capture dust at the cutting point.
  Use a HEPA filter in the vacuum exhaust, and a pre-filter or cyclonic separator to improve vacuum efficiency.
  Use a hose size recommended by the manufacturer.
  Use a hood or shroud that is recommended by the manufacturer
  Must not introduce new hazards, such as obstructing or interfering with safety mechanisms

## Slide 31: Vacuum Dust Collection Controls Continued
  Keep the vacuum hose clear and free of debris, kinks and tight bends
  Follow the manufacturer’s directions on how to reduce dust buildup on the filter.
  Change vacuum-collection bags as needed.
  Set up a regular schedule for filter cleaning and maintenance.
  Avoid exposure to dust when changing vacuum bags and cleaning or replacing air filters.
  Keep the grinder at the appropriate angle.

## Slide 32: Administrative Controls
  Along with the engineering controls, OSHA also requires workplace controls to eliminate exposure to silica dust
  Employers are required to provide training when assigned to a position involving exposure to silica, introduces new protections or needs a refresher.

## Slide 33: PPE Controls
When wet or dust collection controls are not feasible, or do not reduce silica exposures to PEL.
Employer implements a respiratory protection program that complies with OSHA’s 29 CFR 1910.134).
Employee fills out a medical questionnaire
Respiratory fit testing-assigned protection factor (APF) Table 1 as a guide
Wear the model and size of respirator that you were fit tested with
Eliminate facial hair that comes between the sealing surface of the face piece and the face or that interferes with valve function or any other condition that interferes with the seal

## Slide 34: Housekeeping Safe Work Practice Controls
  Standard limits the use of certain cleaning methods to prevent unnecessary exposures to employees
  Do not allow dry brushing or sweeping
  Do not allow the use of compressed air to clear surface areas or clothing unless an efficient ventilation system captures the dust
  Wet sweeping methods can be used when HEPA filtered system is not practical
  Control access to areas through the use of barriers and signage when dust is present

## Slide 35: Classroom Activity-Equipment Demonstration

## Slide 36: Competent Person
The employer must designate a competent person to implement the written exposure control plan
Competent person is an individual capable of
  Identifying existing and foreseeable silica hazards;
  Is authorized to promptly eliminate or minimize these hazards; and
  Has the knowledge and ability to implement the written exposure control plan.
He/she makes frequent and regular inspections of job sites, materials, and equipment
The standard does not require specific training for a competent person.

## Slide 37: Written Exposure Control Plan
Establish and implement a written exposure control plan
Designate a competent person to implement the written exposure plan
Restrict housekeeping practices that expose workers to silica, where feasible alternatives are available
Medical examination to include chest x-ray and pulmonary function testing
Training workers on the work operations that result in silica exposure and ways to limit exposure
Keep records of workers silica exposure and medical examinations

## Slide 38: Alternative Silica Exposure Controls
Employers opting for not to implementing Table 1 must follow the alternative exposure control methods approach
This approach involves:
  Assessing employee exposure to silica
  Limiting exposure to the PEL using feasible engineering and work practice controls
  Providing respiratory protection when necessary.

## Slide 39: Communication of Silica Hazards
  HCS requires employers to inform employees about hazardous chemicals in the workplace, such as respirable crystalline silica, through their written hazard communication programs.
  Written hazard communication programs must describe how the requirements for container labels, safety data sheets (SDSs), and employee training will be met.
  Employers must address at least the health hazards on cancer, lung effects, immune system effects, and kidney effects as part of the hazard communication program for respirable crystalline silica.

## Slide 40: Record Keeping
Per OSHA’s Access to Employee Exposure and Medical Records regulation (29 CFR 1910.1020), employers must maintain records for
  Medical records
  Air monitoring data
  Objective data
Exposure and medical records must be kept and made available to employees, their representatives, and OSHA

## Slide 41: Employee Notification
Employers must notify each affected employee of the results of the exposure assessment within 5 working days of completing it.
  “Affected” means all employees whose exposures were assessed, including employees whose exposures were represented by other employees’ exposure measurements, and those whose exposure assessments were based on objective data.
Employers must either notify each employee in writing or post the results in a location accessible to all affected employees

## Slide 42: Employee Notification with Corrective Action
When an exposure assessment reveals exposures above the PEL, the written notification must also describe the corrective action the employer is taking to reduce employee exposures to or below the PEL.
Corrective actions include engineering controls. However, if engineering controls are not feasible or the employer needs more than 5 days to identify the right engineering controls, respiratory protection is the corrective action that would be described in the written notification.

## Slide 43: This Concludes our Training