## Slide 1
Hazard Communication
Notes: This presentation is designed to assist trainers conducting OSHA 10-hour General Industry outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of 1970 or for any standards issued by the U.S. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the U.S. Department of Labor.

## Slide 2: Introduction
About 32 million workers work with and are potentially exposed to one or more chemical hazards
There are approximately 650,000 existing chemical products, and hundreds of new ones being introduced annually
Chemical exposure may cause or contribute to many serious health effects such as heart ailments, central nervous system damage, kidney and lung damage, sterility, cancer, burns, and rashes
Some chemicals may also be safety hazards and have the potential to cause fires and explosions and other serious accidents
Notes: This is one of the most frequently cited OSHA standards.
This program is intended for workplaces that do not manufacture, import, or distribute hazardous chemicals. Notes have been provided that highlight some of the requirements for these employers. For complete requirements, consult 29 CFR 1910.1200.

## Slide 3: Purpose of OSHA’s Hazard Communication Standard
Hazard Communication
Program
Container
Labeling
Material Safety
Data Sheet
MSDS
Program
Label
To ensure that employers and employees know about work hazards and how to protect themselves so that the incidence of illnesses and injuries due to hazardous chemicals is reduced.
Notes: 29 CFR 1910.1200
The Hazard Communication (HazCom) standard establishes uniform requirements to make sure that the hazards of all chemicals imported into, produced, or used in U.S. workplaces are evaluated, and that this hazard information is transmitted to affected employers and exposed employees.
The HazCom standard is different from other OSHA health rules because it covers all hazardous chemicals. The rule also incorporates a “downstream flow of information,” which means that producers of chemicals have the primary responsibility for generating and disseminating information, whereas users of chemicals must obtain the information and transmit it to their employees.

## Slide 4: Who is covered?
OSHA’s Hazard Communication (HazCom) standard applies to general industry, shipyard, marine terminals, longshoring, and construction employment and covers chemical manufacturers, importers, employers, and employees exposed to chemical hazards.
Notes: 1910.1200(b)
Does the standard apply to an office environment?
Office workers who encounter hazardous chemicals only in isolated instances are not covered by the rule. OSHA considers most office products (such as pens, pencils, adhesive tape) to be exempt under the provisions of the rule. OSHA has stated that intermittent or occasional use of a copying machine does not result in coverage under the rule. However, if an employee handles the chemicals to service the machine, or operates it for long periods of time, then the standard would apply.
“Hazardous Chemical” is any chemical which is a physical or health hazard.

## Slide 5: Employer Responsibilities
Identify and list hazardous chemicals in their workplaces
Obtain Material Safety Data Sheets (MSDSs) and labels for each hazardous chemical, if not provided by the manufacturer, importer, or distributor
Implement a written HazCom program, including labels, MSDSs, and employee training
Communicate hazard information to employees through labels, MSDSs, and formal training programs

## Slide 6: How can workplace hazards be minimized?
The first step in minimizing workplace hazards is to perform a thorough hazard assessment
Employers can rely on the evaluations performed by the manufacturers or importers to establish the hazards of the chemicals they use
  This information is obtained from MSDSs and labels
Notes: Chemical manufacturers and importers must review scientific evidence on the hazards of chemicals they produce or import and report findings to their employees and to employers who distribute or use their products.

## Slide 7: Why is a written program required?
Ensures that all employers receive the information they need to inform and train their employees
Provides necessary hazard information to employees
(f) "Labels and other forms of warning."
(g) "Material safety data sheets."
(h) "Employee information and training."
HazCom Program
Notes: 1910.1200(e)

## Slide 8: Written HazCom Program Requirements
Describes container labeling, MSDSs, and employee training for each workplace
List of the hazardous chemicals
Make information regarding hazards and protective measures available to other employers onsite
Notes: Employer also required to describe how they will inform employees of the hazards of non-routine tasks (for example, cleaning reactor vessels), and the hazards associated with chemicals in unlabeled pipes.

## Slide 9: How must chemicals be labeled?
Identity of the chemical
Appropriate hazard warnings
Name and address of the responsible party
Each container of hazardous chemicals entering the workplace must be labeled or marked with:
Notes: 1910.1200(f)
Chemical manufacturers and importers must convey the hazard information to downstream employers by means of labels on containers and Material Safety Data Sheets (MSDSs). Language used on the warning label does not have to be identical to that on the MSDS.
Chemical manufacturers, importers, and distributors must be sure that containers of hazardous chemicals leaving the workplace are labeled, tagged, or marked with:
- the identity of the chemical,
- appropriate hazard warnings, and
- the name and address of the chemical manufacturer, importer, or other responsible party
Consumer products having labels meeting requirements of the Consumer Product Safety Act do not have to have additional labeling under the HazCom Standard.
Various other chemical products (for example, pesticides, foods, drugs, cosmetics, beverage alcohols) that are subject to labeling laws administered by other Federal agencies are also exempt from the labeling requirements of the HazCom Standard.

## Slide 10: Container Labeling in the Workplace
The hazard warning can be any type of message, picture, or symbol that provides information on the hazards of the chemical(s) and the targeted organs affected, if applicable
Labels must be legible, in English (plus other languages, if desired), and prominently displayed
Notes: Exemptions to the requirement for container labeling:
- Can post signs/placards that convey hazard information if there are a number of stationary containers within a work area with similar contents and hazards
- Can substitute various types of standard operating procedures, process sheets, and similar written materials for container labels on stationary process equipment if they contain the same information and are readily accessible to employees in the work area
- Not required to label portable containers into which hazardous chemicals are transferred from labeled containers and are intended only for the immediate use of the employee who makes the transfer
- Pipes or piping systems, and engines, fuel tanks, or other operating systems in a vehicle, are not considered to be containers

## Slide 11: Material Safety Data Sheets
Physical hazards, such as fire and explosion
Health hazards, such as signs of exposure
Routes of exposure
Precautions for safe handling and use
Emergency and first-aid procedures
Control measures
Prepared by the chemical manufacturer or importer and describe:
Notes: 1910.1200(g)
Chemical manufacturers and importers must develop an MSDS for each hazardous chemical they produce or import, and must provide the MSDS at the time of the initial shipment to a downstream distributor or user. Distributors also must ensure that downstream employers are similarly provided an MSDS.
The MSDSs must be updated by the chemical manufacturer or importer within three months of learning of "new or significant information" regarding the chemical's hazard potential.
OSHA does not require that MSDSs be provided to purchasers of household consumer products (such as "windex" and "white‑out“) when the products are used in the workplace in the same manner that a consumer would use them, i.e.; where the duration and frequency of use (and therefore exposure) is not greater than what the typical consumer would experience. Employees who are required to work with hazardous chemicals in a greater duration and frequency of exposure than a normal consumer have a right to know about the properties of those hazardous chemicals.

## Slide 12: Material Safety Data Sheets (cont’d)
Must be in English and include information regarding the specific chemical identity and common names
Must provide information about the:
  Physical and chemical characteristics
  Health effects
  Exposure limits
  Carcinogenicity (cancer-causing)
  Identification (name, address, and telephone number) of the organization responsible for preparing the sheet
Must be readily accessible to employees in their work area
Notes: In the absence of other employee exposure records, MSDSs that indicate a health hazard are considered employee exposure records under the Access to Employee Medical Records standard, 29 CFR 1910.1020 and must be preserved and maintained for at least thirty years, with some exceptions. [See 29 CFR 1910.1020(d)]
Electronic access is acceptable provided:
- A back-up procedure is available if the electronic system fails
It can be accessed in the employee’s work area
The telephone number provided must be that of a person who can provide additional information about the hazardous chemical and appropriate emergency procedures.

## Slide 13: Material Safety Data Sheets (cont’d)
MSDSs have no prescribed format
If no MSDS has been received for a hazardous chemical, employer must contact the supplier, manufacturer, or importer to obtain one and maintain a record of the contact
Notes: One MSDS may apply to multiple complex mixtures having similar contents and hazards.
For information regarding the preparation of MSDSs, see ANSI Z400.1, Hazardous Industrial Chemicals – Material Safety Data Sheets – Preparation.

## Slide 14: Training
At the time of initial assignment
Whenever a new hazard is introduced into their work area
Training is required for employees who are exposed to hazardous chemicals in their work area:
Notes: 1910.1200(h)
Training is not satisfied solely by giving the employee the data sheets to read. An employer's training program is to be a forum for explaining to employees not only the hazards of the chemicals in their work area, but also how to use the information generated in the hazard communication program. This can be accomplished in many ways (audiovisuals, classroom instruction, interactive video), and should include an opportunity for employees to ask questions to ensure that they understand the information presented to them. Training must be carried out in a language that is comprehensible to the employees.
Training need not be conducted on each specific chemical found in the workplace, but may be conducted by categories of hazard (e.g., carcinogens, sensitizers, acutely toxic agents, irritants, flammables) that are or may be encountered by an employee during the course of his duties.
Employees who have been previously trained by another employer, union, or other entity, do not have to be retrained if the previous training is sufficient to meet the standard’s training requirements for the current work being performed. However, employees must have information about where to find MSDSs in the workplace, who in the company is responsible for the HazCom program, and where to get copies.

## Slide 15: What training is needed to protect workers?
Explanation of the HazCom program, including information on labels, MSDSs, and how to obtain and use available hazard information
Hazards of chemicals
Protective measures such as engineering controls, work practices, and the use of PPE
How to detect the presence or release of a hazardous chemical (using monitoring devices, observation, or smell)

## Slide 16: What information must be provided to workers?
The HazCom standard and its requirements
Operations in their work areas where hazardous chemicals are present
Location and availability of the written hazard evaluation procedures, communications program, lists of hazardous chemicals, and the required MSDSs
Employees must be informed of:

## Slide 17: Summary
OSHA’s Hazard Communication Standard is based on a simple concept - that employees have both a need and a right to know the hazards and identities of the chemicals they are exposed to when working
Employees also need to know what protective measures are available to prevent adverse effects from occurring
Notes: See www.osha.gov for more information on hazard communication, including the following publications:
Hazard Communication Guidelines for Compliance – OSHA 3111
(This is the same information that is contained in Appendix E to 1910.1200 and is also available in Spanish.)
Chemical Hazard Communication – OSHA 3084
(This is also available in Spanish.)